## Slide 1
Module 6 - IVI In-Vehicle Infotainment Systems
Media Service to Audio HAL Message Flow Simulation
Option 3 | Software simulation with traceable Android-style logs
Name
Monikankona Dutta
Department
CSE
Roll No.
4C-54
College
IEM, New Town

## Slide 2
Project Objective
2
Simulate message flow between Media Service and Audio HAL.
Show how HMI actions propagate through the IVI audio stack.
Capture every transition as a readable log and structured trace.
Run repeatable scenarios without Android hardware.
Deliverables
Python source
Android-style logs
CSV trace
JSON summary
Three test scenarios

## Slide 3
Functional Architecture
3
IVI HMI
Play / Pause / Volume
Media Service
Commands + playback state
Audio Service
Focus + routing request
AudioFlinger
Mix + output path
Audio HAL
Open / write / volume / standby
DSP / Amplifier
hardware-facing audio processing
Vehicle Speakers
physical audio output
Message examples
USER_INPUT -> COMMAND_RECEIVED
AUDIO_FOCUS_GRANTED -> START_OUTPUT
WRITE_MIXED_AUDIO -> HAL_WRITE
PAUSE_OUTPUT -> HAL_FLUSH

## Slide 4
Message Types in the Simulation
4
Playback
PLAY, PAUSE, RESUME, NEXT, STOP
Focus
AUDIO_FOCUS_GRANTED
AUDIO_FOCUS_RELEASED
Routing
START_OUTPUT
OPEN_OUTPUT
WRITE_MIXED_AUDIO
HAL
HAL_OPEN
HAL_WRITE
HAL_FLUSH
HAL_STANDBY
A single user action is intentionally traceable across multiple components. This makes the project useful for demonstration, debugging and viva discussion.

## Slide 5
Example Sequence: Play -> Pause
5
User
Media Service
Audio Service
AudioFlinger
Audio HAL
PLAY [track=Highway Drive]
AUDIO_FOCUS_GRANTED [owner=MediaService]
START_OUTPUT
OPEN_OUTPUT
HAL_OPEN [48kHz / 2ch]
PAUSE
PAUSE_OUTPUT
FLUSH

## Slide 6
Repeatable Test Scenarios
6
Normal playback
Play -> volume -> next -> pause -> resume -> stop
Navigation ducking
Play -> reduce volume -> navigation prompt -> restore volume
Call interruption
Play -> focus loss -> pause -> call ends -> resume

## Slide 7
Sample Android-Style Log
7
18:58:39.818 I/IVI_HMI: -> MediaService | USER_INPUT | command=PLAY track=Highway Drive
18:58:39.818 I/MediaService: -> MediaService | COMMAND_RECEIVED | command=PLAY track=Highway Drive
18:58:39.818 I/AudioService: -> AudioFlinger | AUDIO_FOCUS_GRANTED | owner=MediaService
18:58:39.818 I/AudioService: -> AudioFlinger | START_OUTPUT
18:58:39.818 I/AudioFlinger: -> AudioHAL | OPEN_OUTPUT
18:58:39.818 I/AudioHAL: -> DSP/Amplifier | HAL_OPEN | sample_rate=48000 channels=2
18:58:39.818 I/AudioFlinger: -> AudioHAL | WRITE_MIXED_AUDIO | frames=1024
18:58:39.818 I/AudioHAL: -> DSP/Amplifier | HAL_WRITE | frames=1024
18:58:39.818 I/MediaService: -> IVI_HMI | STATE_UPDATE | state=PLAYING track=Highway Drive
18:58:39.818 I/IVI_HMI: -> MediaService | USER_INPUT | command=VOLUME value=0.75
18:58:39.818 I/MediaService: -> MediaService | COMMAND_RECEIVED | command=VOLUME value=0.75

## Slide 8
Implementation Structure
8
Core model
Message
TraceLogger
MediaService
AudioService
AudioFlinger
AudioHAL
Outputs
session_logcat.txt
message_trace.csv
summary.json
Testing
Normal scenario
Navigation scenario
Call interruption
Automated unit tests
Runtime dependency: Python standard library only.

## Slide 9
Validation Results
9
Scenario | Messages | HAL events
normal | 39 | 7
navigation | 26 | 5
call | 32 | 5
Automated checks passed for HAL command generation, call interruption/resume sequencing and output-summary consistency.

## Slide 10
Conclusion and Future Scope
10
The simulator fulfills the selected Module 6 message-flow objective.
User actions remain traceable from HMI to Media Service and Audio HAL.
The output is repeatable, testable and easy to demonstrate.
Future work: run the same sequence inside Android Automotive with real logcat capture.

## Slide 11
Thank You